## Slide 1: Chapter 5
1
The Cellular Concept

## Slide 2: Outline
2
Cell Shape
  Actual cell/Ideal cell
Signal Strength
Handoff Region
Cell Capacity
  Traffic theory
  Erlang B and Erlang C
Cell Structure
Frequency Reuse
Reuse Distance
Cochannel Interference
Cell Splitting
Cell Sectoring

## Slide 3: Cell Shape
Cell
R
(a) Ideal cell
(b) Actual cell
R
R
R
R
(c) Different cell models
3

## Slide 4: Signal Strength
Select cell i on left of boundary Select cell j on right of boundary
Ideal boundary
Cell i
Cell j
-60
-70
-80
-90
-100
-60
-70
-80
-90
-100
Signal strength (in dB)
4

## Slide 5: Signal Strength
Signal strength contours indicating actual cell tiling. This happens because of terrain, presence of obstacles and signal attenuation in the atmosphere.
-90
-100
5
-60
-70
-80
-60
-70
-80
-90
-100
Signal strength (in dB)
Cell i
Cell j

## Slide 6: Handoff Region
BSi
Signal strength due to BSj
Signal strength
due to BSi
j
4
2
5
X1 X3 X X X X
th
MS BS
E
Pmin
Pi(x)
Pj(x)
By looking at the variation of signal strength from either base station it is possible to decide on the optimum area where handoff can take place.

## Slide 7: Cell Capacity
Average number of MSs requesting service (Average arrival rate): 
Average length of time MS requires service (Average holding time): T
Offered load: a = T
e.g., in a cell with 100 MSs, on an average 30 requests are generated during an hour, with average holding time T=360 seconds.
Then, arrival rate =30/3600 requests/sec.
A channel kept busy for one hour is defined as one Erlang (a), i.e.,
a  30 Calls  360 Sec  3 Erlangs
3600 Sec call

## Slide 8: Cell Capacity
Average arrival rate during a short interval t is given by t
Assuming Poisson distribution of service requests, the probability P(n, t) for n calls to arrive in an interval of length t is given by
 t n
 t
n !
P ( n , t )  e
Assuming  to be the service rate, probability of each call to terminate during interval t is given by t.
Thus, probability of a given call requires service for time t
or less is given by
s(t )  1  e   t

## Slide 9: Erlang B and Erlang C
Probability of an arriving call being blocked is
,
i!
1
S

i1
ai
S!
S
BS, a  a 
where S is the number of channels in a group.
Probability of an arriving call being delayed is
Erlang B formula
Erlang C formula
where C(S, a) is the probability of an arriving call being delayed with
a load and S channels.

## Slide 10: Efficiency (Utilization)
Efficiency  Traffic nonblocked
Capacity
 Erlangs  portions of nonrouted traffic Number of trucks (channels)
Example: for previous example, if S=2, then
B(S, a) = 0.529, ------ Blocking probability, i.e., 60% calls are blocked.
Total number of rerouted calls = 30 x 0.6 = 18 Efficiency = 3(1-0.529)/2 = 0.7065

## Slide 11: Cell Structure
F3
F1 F2
F3
F1 F2
F3
F4
F1 F2
F3
F5 F4
F6 F1
F7 F2
(a) Line Structure
(b) Plan Structure
Note:
Fx is set of frequency, i.e., frequency group.

## Slide 12: Frequency Reuse
F3
F7 F2
F3
F7 F2
F3
F6 F1
F5 F4 F7 F2
F3
F5 F4
F6 F1
F5 F4 F7 F2
F6
F6
F5 F4
Fx: Set of frequency
7 cell reuse cluster
Reuse distance D
F1
F1
F1
F1
Same frequency can be used in multiple cell which are far apart

## Slide 13: Reuse Distance
F3
F7 F2
F3
F5 F4
F6 F1
F5 F4 F7 F2
F6
Reuse distance D
For hexagonal cells, the reuse distance is given by
D  3N R
where R is cell radius and N is the reuse pattern (the cluster size or the number of cells per cluster).
Reuse factor is
R
3N
R
D 
Cluster
F1
F1

## Slide 14: Reuse Distance (Cont’d)
The cluster size or the number of cells per cluster is given by
N  i2  ij  j 2
where i and j are integers.
i
N = 1, 3, 4, 7, 9, 12, 13, 16, 19, 21, 28, …, etc.
The popular value of N being 4 and 7.
j
60o

## Slide 15: Reuse Distance (Cont’d
15
i = 3
j = 2
N = 9 + 3*2 + 4
= 19

## Slide 16: How to form a Cluster
16

## Slide 17: How to form a Cluster
17
Here j = 1
N = The number of cell to be clustered
Frequency Label L whose center is at (u, v):

## Slide 18: Example
18
N = The number of cell to be clustered
Given, N =7, Then i = 2

## Slide 19: Cochannel Interference
Mobile Station
Serving Base Station
First tier cochannel Base Station
Second tier cochannel Base Station
R
D2
D3
D4
D6
D5
D1
D

## Slide 20: Cochannel Interference
Cochannel interference ratio is given by

M

k
I
C  Carrier C I Interference
k 1
where I is co-channel interference and M is the maximum number of co-channel interfering cells.
For M = 6, C/I is given by
where  is the propagation path loss slope and  = 2~5.

## Slide 21: Worst Case of Cochannel Interference
Mobile Station
Serving Base Station
Co-channel Base Station
R
D1
D2
D3
D4
D5
D6
Here, q= D/R

## Slide 22: Cell Splitting
22
The BSs of all cells transmit information at the same power level so that the net coverage area for each cell is the same.
Resource demand may depend on the density of users in a given area.
Need to split a cell into several small cells with the increased number of traffics.
Additional BSs need to be established at the center of each new cell so that higher density of calls can be handled effectively.

## Slide 23: Cell Splitting
Large cell (low density)
Small cell (high density)
Smaller cell (higher density)
Depending on traffic patterns the smaller cells may be activated/deactivated in order to efficiently use cell resources.

## Slide 24: Cell Sectoring by Antenna Design
60o
120o
(a). Omni
(b). 120o sector
(e). 60o sector
120o
(c). 120o sector (alternate)
a
b
c
a
b
c
(d). 90o sector
90o
a
b
c
d
a
b
c
d
e
f

## Slide 25: Cell Sectoring by Antenna Design
it requires coverage of a smaller area by each antenna and hence lower power is required in transmitting radio signals
It also helps in decreasing interference between co-channels
Placing directional transmitters at corners where three adjacent cells meet.
C
B
X
A